## Slide 1
A Trunking Solution over Operator Network
eChat Trunking Solution

## Slide 2
eChat solution takes the wide-area trunking service as the core requirement.
Provides multi-scenario convergence services for the industrial customers.
Create the best Internet + digital trunking service platform.
Operator Network
Intenet
eChat Radio
eChat Servers
Dispatch Console
Management Console
Operator Network Trunking Solution – eChat

## Slide 3
Overview of eChat Solution

## Slide 4: eChat System Architecture
Service Platform
2G/3G/4G/Wi-Fi Network
Management Console
PLMN
PSTN
Internet
Dispatching
Console
Data Base
Terminal
Handheld Radio
Vehicle Mounted Radio
Servers
External System
Switch
Operator Network
Gateway

## Slide 5
OTA
PDS
LDS
VDS
DRS
eChat servers
MMS
PHR
LMS
Internet
Management Console
Dispatch Console
Mandatory
Optional
Switch
eChat System Architecture
Firewall
All of the network elements support load sharing and disaster redundancy!

## Slide 6
eChat Server Description
PDS
Control center of the PTT voice service
PHR
Management of users and groups authentication
LDS
Management of the users and groups location
MMS
Management of messages, images and multimedia files
LMS
For the user login and registeration
OTA
For the user remotely update APK
VDS
Control center of the video service
DRS
Storage of voice and video recording data
Notes:   PDS-PTT Dispatching server
  PHR-PTT Home Register
  LDS-Location Dispatching server
  MMS-Multimedia message server
  LMS-Local maintenance server
  OTA-Over the air
  VDS-Video Dispatching server
  DRS-Data recording server

## Slide 7: eChat Solution – Key Technologies
Trunking Features
  Push-To-Talk:: Press the PTT button and then talk
  One-to-many call: Large call capacity and instant communication with many members
Key Technologies
  Multi-mode Access Network
    Our eChat service is independent of the bearer network, so that it can be performed in different access networks, such as 2G, 3G, 4G and Wi-Fi.
  Modularization and Distributed Design
    Our eChat system adopt modularization and distributed technology to design, it can be deployed according to different capacity scenarios.
    The distributed technology may ensure the system redundancy, stability and service continuity.
    The modularization design to make the future expansion easy and fast.
    Our eChat system support PC server or cloud based deployment.

## Slide 8: eChat Solution Features
  Dispatch Console
  Dispatching
  Temporary group call
  Status Subscription
  Local Voice Recording
  Triple Screens
  Management Console
  Agent Management
  User Account Management
  Fleet and Group Management
  Organization Management
  System Maintenance
  Management Data Import and Export
  Positioning
  Real-Time Location
  Historical Track
  Circle Selection Call
  Ranging
  Geo-fencing
  Location Data Export
  Unified Storage
  Unified Voice Storage
  Unified Video Storage
  Reliability
  OTA
  System Data Disaster Recovery
  Interconnection
  Interconnection with DMR
  Interconnection with TETRA
  Interconnection with LTE B-TrunC
  Industry Customization Service
  911 Alarm Tri-party Call
  Merchant One-Click Alarm
  Logo Customization
  Roll Call in Dispatch Console
  High Priority Group
  Map Industry Layer Display
  Secondary Development Interface
  Voice
  Group call
  Half-Duplex Private Voice Call
  Full-Duplex Private Voice Call
  Floor Priority
  Late Entry
  Information Synchronization and Update
  Emergency Alarm (under developing)
  Call Status Indication
  User Status Indication
  Data
  Multimedia Message
  Location Information Delivery
  Video
  Video Backhaul
  Video Push
  Video Forwarding and Distribution
  Concurrency of Voice and Video Service
  Multiple Video Sources Supporting
Notes: White: Basic Features/Yellow: Advanced Features/Orange: Customized Features

## Slide 9: eChat Solution Roadmap
  Terminal Service
  Support temporary group call on terminal with large screen
  APK adaptation for e700
  Support IP camera
  Voice Service
  High priority group call
  SMS/MMS Service
  Send picture with location information
  Quality of Service
  Power consumption reduction and speech quality improvement
  Management console concurrent capability improvement
  Interconnection
  Interconnect with GoTa system
V5.80.20
V5.80.30
V5.80.40
V5.80.10
  Operation Management Service
  Account with terminal and SIM card binding
  One-Click alarm service access control management
  Management console support interconnection account
  Management console support hierarchical management
  Dispatch Service
  Dispatch console support multi voice dispatch mode
  Dispatch console support local video recording
  Dispatch console ease of use improvement
  System Deployment
  Support PC server based Mini eChat deployment
  Voice Service
  Inter-group call priority
  Dispatch Service
  Dynamic regrouping
  Emergency alarm
  Support map-based third party industry layer
  Circle selection call support SMS/MMS
  Support industry user use different icon to display
  Terminal Service
  Voice local recording
  Video local recording and storage
  Data Service
  SMS/MMS support read receipt
  Broadcasting message
  Video Service
  Video dispatch service support accompanying sound
  Site enforcement recorder access
  Operation Management Service
  Terminal model white list control
  System capacity license control
  Voice Service
  Voice encryption
  Dispatch Service
  Remote stun/revive
  All subscribers locating
  Operation Management Service
  Video service license control
  Storage service license control
  Online/offline user data export
  Voice service statistics export
  Video service statistics export
  Message service statistics export
  Video Service
  Terminal transfer video and foward a copy to dispatch console
  System Deployment and Reliability
  Support board-based Mini eChat deployment
  Support main and standby Mini eChat deployment
2018.12.30
2019.06.30
2019.12.30
  Released
  Developing
  Planned
Planning
2018.06.30

## Slide 10: Group Call
A radio or dispatcher initiate a half-duplex voice group call.
All group members must press the PTT button to talk.
If a user request for the floor when someone is talking, the user must queue up to wait or take over the floor who is talking.
Floor Request

## Slide 11: Private Call
Private call means a one-to-one call during which other users cannot hear the conversation.
A private call can be initiated by a radio or a dispatcher.
The system support half-duplex voice private call and full-duplex voice private call.
Dispatcher

## Slide 12: Priority Service, Working First
Floor Priority
  The member with high priority talk first, which ensures that important work first.
  The members with the same priority queue up to talk, which ensures well-organized communication.
High Priority Group
  Users belong to both general group and high priority group.
  If a high priority group initiate a call when a general group is calling, users who belongs to these two groups will be disconnected from the general group forcibly and then join the high priority group.
  Emergency Alarm
  Users who has the privileges may initiate an emergency alarm in case of emergency. When initiating emergency alarm, the default dispatcher will received the alarm, and the user's location will be shown on the map, the video will be pulled up to the default dispatch console.

## Slide 13: Dispatching Console
Voice Dispatch
Location Service
Video Dispatch
  Voice dispatch, private call, group call, record and replay.....
  Location service, user location, group location, track and replay.....
Video dispatch, video pull, video distribution, screen record, snapshot, screen capture.....
MSG service, SMS/MMS, text message, picture, video, file transmitting.....
History, storage service, video record, audio record, local record, electronic fence, multimedia message.....
MSG Service

## Slide 14: Video Backhaul
Backhaul
Pull-up by dispatcher
  Video backhaul means a one-way video session initiated by the radio or dispatcher.
  Dispatcher video pull-up means pulling the video of the specified radio or camera to the dispatch console.
  Radio video pull-down refers to the radio may pull video from other radios or cameras.

## Slide 15: Video Push
Real-time video push from the radio
Push
  The video push service is initiated by radio.
  A radio can push its local real-time video to other radios, dispatch console and groups.

## Slide 16: Video Forwarding and Distribution
Real-time video push from the radio
Push
Distribution
  A dispatcher can forward the received video to other dispatch consoles or handheld radios, or send the video to the TV wall, achieving cooperative video dispatch of multiple dispatch consoles and video users.
Distribution
Distribution

## Slide 17: eChat Interconnection with DMR
eChat Platform
2G/3G/4G/Wi-Fi
Handheld Radio
Vehicle Mounted Radio
uGW
The uGW is a gateway which may interconnect eChat with DMR.
Unified management and unified dispatching.
DMR Core Network
DMR BS
Handheld
Radio
Vehicle Mounted Radio
Management Console
Dispatching
Console
Data Base
Servers

## Slide 18: eChat Trunking System – Highlights
Operator network, interconnection with operator's core network, access network, bear network, providing QoS-based trunking services.
Low TCO, NO need dedicated frequency band, NO need dedicated network, providing QoS-based trunking services over operator network.
Interconnection with traditional dedicated trunking systems, such as DMR, TETRA and B-TrunC.
End-to-end solution, provide service platform, radios, dispatch console, management console.
PC server or cloud based deployment of service platform, distributed load sharing and redundancy protection, easy for expansion and upgrade.
MCPTT evolution, our eChat system support Mission Critical Push-To-Talk evolution.
Distributed eChat system support unlimitation capacity expansion.

## Slide 19
Products

## Slide 20
GH65X
e700
e350
GH910
GH820
VPN / Internet
MSG Service
PoC
Dispatch
Voice Dispatch
Video Dispatch
Location Service
Management
eChat Management Platform
Terminals
Transmission
GH880B
(Developing)
(Developing)

## Slide 21: eChat Platform Portfolio
mini-eChat5000_1
Voice/Location/Message
Voice/Location/Message/Video/Storage
mini-eChat5000_2
1x Server
1x fixed IP address
Up to 5K users
2x Server
2x fixed IP address
Up to 5K users
Up to 50 video streamings
Distributed eChat
Voice/Location/Message/Video/Storage
5x Server
2x fixed IP address
Up to 10K users, extension capable with more servers
Up to 100 video streaming(720P),or 200 VGA streamings
mini-eChat2000
1x Server
1x fixed IP address
Up to 2K users
Up to 8 video streamings

## Slide 22
Minimized eChat Platform
Aimed at Small-sized/Medium-sized Channel or Enterprise Customers
Support Basic and Advanced Features
Support PC Server or Cloud Based Deployment
Support 2000 or 5000 System Capacity
Support Interconnection with Other Systems
Mini-eChat Product Introduction

## Slide 23
Mini-eChat Product Configuarion
Mini-eChat_2000
 |  | Mini eChat 2000 (Basic and Advanded Features) |  | 
 |  | Configuration | Description | Remark
Voice service processing unit (PDS) |  | √ | Stand alone | 1. All of the service units will be deployed in one server. 2. All of the service units does NOT support expansion, tailoring and customization.
Database unit (PHR) |  | √ |  | 
Login management service unit (LMS) |  | √ |  | 
Online upgrade service unit (OTA) |  | √ |  | 
Location service processing unit (LDS) |  | √ |  | 
Multimedia message service processing unit (MMS) |  | √ |  | 
Video service processing unit (VDS) |  | √ |  | 
Data Storage unit (DRS) |  | √ |  | 
Interconnection GateWay (uGW) |  | Optional | Stand alone | Optional for interconnect with the other private trunking system.
Agents | Dispatching Console | Optional | ≧1 | Agent used for management and dispatching.
 | Management Console | Optional |  | 
Switch |  | √ | ≧1 | Mandatory, used for connect all servers.
Firewall |  | √ | ≧1 | Mandatory, used for protect all servers.
Scenarios
Configuration Options

## Slide 24
Mini-eChat Product Configuarion
Mini-eChat_5000_1
 |  | Mini eChat 5000_1 (Voice/Location/SMS/MMS Only) |  | 
 |  | Configuration | Description | Remark
Voice service processing unit (PDS) |  | √ | Stand alone | 1. This scenario will deploy PDS, PHR, LMS, OTA, LDS and MMS service units only, all of above service units will be deployed in one server. 2. All of above deployed service units does NOT support expansion, tailoring and customization.
Database unit (PHR) |  | √ |  | 
Login management service unit (LMS) |  | √ |  | 
Online upgrade service unit (OTA) |  | √ |  | 
Location service processing unit (LDS) |  | √ |  | 
Multimedia message service processing unit (MMS) |  | √ |  | 
Video service processing unit (VDS) |  |  |  | 
Data Storage unit (DRS) |  |  |  | 
Interconnection GateWay (uGW) |  | Optional | Stand alone | Optional for interconnect with the other private trunking system.
Agents | Dispatching Console | Optional | ≧1 | Agent used for management and dispatching.
 | Management Console | Optional |  | 
Switch |  | √ | ≧1 | Mandatory, used for connect all servers.
Firewall |  | √ | ≧1 | Mandatory, used for protect all servers.
Scenarios
Configuration Options

## Slide 25
Mini-eChat Product Configuarion
Mini-eChat_5000_2
 |  | Mini eChat 5000_2 (Basic and Advanded Features) |  | 
 |  | Configuration | Description | Remark
Voice service processing unit (PDS) |  | √ | Stand alone | 1. This scenario will deploy all of the service units, the PDS, PHR, LMS, OTA, LDS and MMS will deployed in one server. 2. The VDS and DRS service units will be deployed in another server. 3. All of the service units does NOT support expansion, tailoring and customization.
Database unit (PHR) |  | √ |  | 
Login management service unit (LMS) |  | √ |  | 
Online upgrade service unit (OTA) |  | √ |  | 
Location service processing unit (LDS) |  | √ |  | 
Multimedia message service processing unit (MMS) |  | √ |  | 
Video service processing unit (VDS) |  | √ | Stand alone | 
Data Storage unit (DRS) |  | √ |  | 
Interconnection GateWay (uGW) |  | Optional | Stand alone | Optional for interconnect with the other private trunking system.
Agents | Dispatching Console | Optional | ≧1 | Agent used for management and dispatching.
 | Management Console | Optional |  | 
Switch |  | √ | ≧1 | Mandatory, used for connect all servers.
Firewall |  | √ | ≧1 | Mandatory, used for protect all servers.
Scenarios
Configuration Options

## Slide 26
Distributed eChat Product Introduction
Distributed eChat Platform
Aimed at Medium-sized/Large-sized Channel or Operator Customers
Support Basic and Advanced Features
Support Industry Customization Features
Support PC Server or Cloud Based Deployment
Support 10000+ Active User Capacity and Unlimitation Expansion
Support Interconnection with Other Systems

## Slide 27
Distributed eChat Product Configuration
 |  | Distributed eChat System (All Features) |  | 
 |  | Configuration | Description | Remark
Voice service processing unit (PDS) |  | √ | Stand alone/ Load sharing | PDS support load sharing according to the voice service traffic.
Database unit (PHR) |  | √ |  | 
Login management service unit (LMS) |  | √ | Stand alone | 1. LMS support distributed deployment according to the accessed subscribers. 2. LMS support N+1 backup.
Online upgrade service unit (OTA) |  | √ |  | 
Location service processing unit (LDS) |  | Optional | Stand alone/ Load sharing | 1. LDS support load sharing according to the location service traffic. 2. Storage space for location service may expand by add hard disk.
Multimedia message service processing unit (MMS) |  | Optional |  | 1. Optional for short message service and multimedia message service. 2. MMS support load sharing according to the SMS/MMS service traffic.
Video service processing unit (VDS) |  | Optional | Stand alone/ Load sharing | 1. Optional for video service. 2. VDS support load sharing according to the video service traffic.
Data Storage unit (DRS) |  | Optional | Stand alone/ Load sharing | 1. Optional for voice storage and video storage. 2. DRS support load sharing according to the stroage service traffic.
Interconnection GateWay (uGW) |  | Optional | Stand alone | Optional for interconnect with the other private trunking system.
Agents | Dispatching Console | Optional | ≧1 | Agent used for management and dispatching.
 | Management Console | Optional |  | 
Switch |  | √ | ≧1 | Mandatory, used for connect all servers.
Firewall |  | √ | ≧1 | Mandatory, used for protect all servers.
Scenarios
Configuration Options

## Slide 28
eChat Trunking System – Typical Specification
Item | Mini eChat 2000 | Mini eChat 5000 | Distributed eChat
Maximum online users | 2,000 | 5,000 | ≧10,000(Expandable)
Maximum online groups | 100 | 200 | ≧1,000(Expandable)
Maximum concurrent voice calls | 100 | 200 | ≧1,000(Expandable)
Maximum concurrent 720P video backhaul | 8 | 50 | ≧100(Expandable)
Concurrent location users (30 seconds interval) | 2000 | 5000 | ≧10,000(Expandable)
Number of concurrent voice recordings | 50 | 100 | ≧100(Expandable)
Number of concurrent video recordings | 5 | 10 | ≧50(Expandable)
Maximum record storage period | 90 days | 90 days | 90 days
Server Quantity(Dell PER740) | 1 | 2 | ≧5 ( Expandable)

## Slide 29
Configuration Option | Mini eChat 2000 | Mini eChat 5000 | Distributed eChat
Voice service processing unit (PDS) | DELL PER740 | DELL PER740 | DELL PER740
Database unit (PHR) |  |  | 
Login management service unit (LMS) |  |  | DELL PER740
Online upgrade service unit (OTA) |  |  | 
Location service processing unit (LDS) |  |  | DELL PER740
Multimedia message service processing unit (MMS) |  |  | 
Video service processing unit (VDS) |  | DELL PER740 | DELL PER740
Data Storage unit (DRS) |  |  | DELL PER740
Interconnection GateWay (uGW) | DELL PER640/740 | DELL PER640/740 | DELL PER640/740
Agent (Dispatch Console/Management Console) | PC | PC | PC
Terminal | e350/e700/GH651A/GH820/GH880B/GH910 |  | 
eChat Trunking System – Typical Configuration

## Slide 30: mini-eChat Migration to Distributed eChat (1)
mini-eChat5000_1
Voice/Location/Message
Voice/Location/Message/Video/Storage
mini-eChat5000_2
1x Server
1x fixed IP address
Up to 5K users
2x Server
2x fixed IP address
Up to 5K users
Up to 50 video streamings(720P)
Distributed eChat
Voice/Location/Message/Video/Storage
5x Server
2x fixed IP address
Up to 10K users, extension capable with more servers
Up to 100 video streaming(720P),or 200 VGA streamings

## Slide 31: mini-eChat Migration to Distributed eChat (2)
Voice/Location/Message/Video/Storage
mini-eChat2000
1x Server
1x fixed IP address
Up to 2K users
Up to 8 video streamings(720P)
Distributed eChat
Voice/Location/Message/Video/Storage
5x Server
2x fixed IP address
Up to 10K users, extension capable with more servers
Up to 100 video streaming(720P),or 200 VGA streamings

## Slide 32: Terminal - e350 handheld radio
eChat PTT
LTE-FDD: B1/B2/B3/B4/B5/B7/B8/B20/B28
LTE-TDD: B38/39/40/41
WCDMA: B1/B2/B5/B8
Small and portable, 88 * 54.5 * 29.8mm, 200g
Loud speaker, 1W Power Rating
Voice assistance optional
1.3 inch B&W LCD , 128x48 display
GPS/AGPS
4000mAh battery
IP54
e350

## Slide 33: Terminal - e700 handheld radio
eChat PTT
Network: WCDMA/LTE
LTE-FDD: B1/3/20/28
LTE-TDD: B38/39/40/41
WCDMA: B1/B8
4.0 inch, 800*480, LCD touchable display
Wi-Fi, BT
13M pixels rear camera
VoLTE
GPS/AGPS
4000 mAh battery
IP54

## Slide 34: Professional Terminal - GH651A handheld radio
eChat PTT
LTE-FDD: B3/B20/B31
Wi-Fi
DMO
Professional radio design
2.2 inch LCD and keypad
Android OS
Camera back & front
GPS/BDS
Multiple sensors integrated supporting various apps
IP67

## Slide 35: Smart Terminal – GH880B
GH880 eChat
eChat PTT
LTE-TDD: B38/B39/B40/B41
LTE-FDD: B1/B3/B5/B7/B8/B20/B31
WCDMA: B1
GSM: B2/B3/B5/B8
DMO
Screen: 4.8-inch high definition LCD
Front & Rear camera: 5 &13 megapixels, CMOS
Wi-Fi, BT, NFC
Battery: 4500 mAh
IP67

## Slide 36: Smart Terminal – GH820
GH880 eChat
eChat PTT
LTE-FDD: B1/B3/B5/B7/B8/B20/B28
LTE-TDD: B38/B39/B40/B41
WCDMA: B1/B2/B5/B8
GSM: B2/B3/B5/B8
Screen: 5.7-inch high definition LCD
Front & Rear camera: 13 megapixels, CMOS
Wi-Fi, BT, NFC
Battery: 3500 mAh
IP67

## Slide 37: Dual Model Terminal – GH910
GH880 eChat
eChat PTT
LTE and DMR dual mode
LTE FDD: B1/B3/B5/B7/B8
LTE TDD: B38/B39/B40/B41
WCDMA: B1/B8
GSM: B2/B3/B5/B8
DMR: UHF1
Screen: 4.0-inch high definition LCD
Front & Rear camera: 13 megapixels, CMOS
Wi-Fi, BT, NFC
Battery: 4000 mAh
IP67

## Slide 38: Professional Terminal - GM651A Vehicle Mounted Radio
eChat PTT
FDD-LTE: B3/B20/B31
DMO
Wi-Fi
5.0 inch touchscreen and keypad
Android OS
Support external USB/IP camera
GPS/BDS
IP54
GM655 eChat

## Slide 39
Cases

## Slide 40
Application Scenarios
Hospitals
Logistics
Factory
Airport
City Utilities
Sea Ports
Construction
Trafic Police
Water Supply
Taxi
Customs
First Aid
Oil Field
Tranportation

## Slide 41: eChat Trunking System Global Footprint
Spain
China
Indonesia
Pakistan
Colombia
Kenya
South Africa
Turkey